## Slide 1: A Seamless Phase 2A-Phase 2B Multi-Center Trial to test the Benefits of Benfotiamine on the Progression of Alzheimer’s disease (BENFOTEAM)
Biospecimen Collection and Shipment training

## Slide 2: Content
Biospecimen Collection Schedule
Kit Request Module
Specimen Labeling Instruction
Specimen Collection and Processing
Shipment Packaging and Forms
Creating Airbills and Scheduling Pick Ups
Other Requirements: MTAs, IATA Training
Non-Conformance Issues
NCRAD Resources and Contact

## Slide 3: Benfotiamine Biospecimen Collection Schedule
 | Pre-Dose |  |  |  | Post Dose |  |  |  | Optional
 | Whole Blood | Plasma | Buffy Coat | Washed Erythrocyte | Whole Blood | Plasma | Buffy Coat | Washed Erythrocyte | CSF
Screening |  | X | X |  |  |  |  |  | 
Baseline | X | X | X | X | X | X | X | X | X
Week 8 | X | X | X | X | X | X | X | X | 
Week 72 | X | X | X | X |  |  |  |  | X

## Slide 4: Kit Request Module
Ordering Blood Kit Supplies
  Ex: tubes, pipettes, labels, cryobox
Ordering Frozen Shipment Supplies
  Ex: styrofoam container, cardboard shipper, shipping stickers
Allow for three weeks from time of order to receipt of supplies
    Initial order should be received prior to site start date

## Slide 5: Kit Request Module Instruction
Verify site shipping address and contact information
Enter kit order amount
  Screening Kit->Screening Shipping Kit
  Baseline, Week 8, Week 72->Batch Shipping Kit
  All screening visits must be entered into screening tracker prior to shipping. Reminder in kit request module
  Supplemental kit will be sent with initial order. This kit contains the saline needed for washed RBCs. Only one supplemental kit should be order per year.
*Allow for 3 weeks for kits to arrive when placing order
www.kits.iu/BENFO
Notes: Please do not order in bulk. Kits do expire. Plan for a month in advanced

## Slide 6: BENFO Screening Reporter www.kits.iu.edu/BENFOScreening
Enter date of each screening visits and Participant ID
Tracker allows for 3 screening visits per form. If there are more than 3 screening visits scheduled, submit another survey.
Allows for efficient processing to return inclusion/exclusion results

## Slide 7: GUID (Globally Unique Identifier)
The GUID is a participant ID that allows researchers to share data specific to a study participant, without exposing personally identifiable information.
Participation is optional. If a patient chooses to participate:
1. Create an account: https://bricsguid.nia.nih.gov/portal/jsp/login.jsp
2. Once you have an account, go to the GUID Tool – Create GUID
3. To open the ‘Launch GUID Tool’ you will need to have Java installed on your device
4. In order to generate a GUID, the following PHI is required on the Appendix A.

## Slide 8
Specimen Labeling Instruction

## Slide 9: Specimen Labels
Ties all biospecimens and kit content together for each participant
Placed on Cryobox and Blood Sample and Shipment Notification Form
Kit Number Label
Participant ID Label
Collection Tube/Aliquot Label
Handwritten by sites according to unique study ID
Placed on blood collection EDTA tubes
Specific to type of biospecimen
Contains unique Specimen# and Kit#
Place on EDTA tube and processed cryovials

## Slide 10: Specimen Labeling Instruction: Label Placement Details
Write site ID and participant ID with fine-point marker prior to label placement
Place all labels on Whole-Blood EDTA 10 ml tube and Cryovial 2 ml before blood collection, processing, or freezing
Label collection tubes and cryovials for one participant at a time to avoid mix ups.
Wrap labels horizontally and adhere completely to all tubes
Collection Tube Label Diagram
Aliquot
Label Diagram

## Slide 11: Specimen Collection and Processing

## Slide 12: Benfotiamine Biospecimen Samples
NCRAD will provide training and materials for the following biospecimens collected:
  Whole Blood
  Plasma
  Buffy Coat
  Washed RBCs
  CSF (Optional)

## Slide 13
Sample Type | Cryovial Cap Color | Example:
Whole Blood | Yellow | 
Plasma | Purple | 
Residual Plasma | Blue | 
Buffy Coat | Clear | 
Washed RBC | Red | 
Local Lab CSF | Yellow | 
Processed CSF | Clear | 
Residual CSF | Blue | 

## Slide 14
SCREENING VISIT- PROCESSING PLASMA AND BUFFY COAT ONLY

## Slide 15: Specimen Collection and Processing: Plasma and Buffy Coat Collection (Screening)
50 ml Conical with 30 ml pooled plasma after inversion
Retrieve buffy coat from each EDTA (expected to have reddish color from RBCs)
Cryobox #1
20 purple-capped - 0.5 ml of plasma
Cryobox #2
5 purple-capped – 1.0 ml of plasma
1 blue-capped – <0.5 ml residual plasma
3 clear-capped – ~1.0 ml buffy coat
Plasma
Buffy Coat
Red Blood Cells

## Slide 16
BASELINE, WEEK 8, WEEK 72
Processing Whole-Blood, Plasma, Buffy Coat, and Washed RBCs

## Slide 17
BASELINE, WEEK 8, WEEK 72
Processing Whole-Blood, Plasma, Buffy Coat, and Washed RBCs

## Slide 18
Cryobox #1
20 purple-capped - 0.5 ml of plasma
Cryobox #2
5 purple-capped – 1.0 ml of plasma
1 blue-capped – >1.0 ml residual plasma
3 clear-capped – ~1.0 ml of buffy coat
1 yellow-capped – 1.0 ml of whole blood
1 red-capped – 1.5 ml of washed RBCs
Visit | Pre-Dose | Post-Dose
Baseline | X | X
Week 8 | X | X
Week 72 | X | 

## Slide 19
Optional Baseline and Week 72
CSF Preparation

## Slide 20
Shipment Packaging, Labeling, & Forms

## Slide 21: Frozen Shipment Packaging
All samples shipped frozen to NCRAD Monday-Wednesday ONLY
Hold packaged samples in a -80°C freezer until pickup
Include copy of Blood Sample and Shipment Notification Form in shipper
Screening visit-ship quickly & individually (2 cryoboxes)
All other visits-batch samples together (8 cryoboxes)
Sites provide dry ice for shipments
~10 lbs. per single shipper (screening). ~45 lbs. per batch shipment (visits)

## Slide 22: Frozen Shipment Tutorial
https://ncrad.org/shipping_address.html

## Slide 23: Specimen Packaging and Shipment: Frozen Specimen Packaging
Step 1. Place frozen cryobox in biohazard bag with absorbent sheet
Important: Confirm kit number label has been placed on the outside of cryobox

## Slide 24: Specimen Packaging and Shipment: Frozen Specimen Packaging
Step 2. Place 2-3 inches of dry ice in the bottom of the styrofoam shipping container
Step 3. Insert cryoboxes with tubes upright
Step 4. Fully cover all cryoboxes with 2 inches of dry ice
Reminder:
Screening Shipper holds 2 cryoboxes
Batch Shipper holds 8 cryoboxes
Notes: If samples freeze at an angle or upside down it ruins the quality of the sample.

## Slide 25: Blood Sample and Shipment Notification Form
Step 5.Include Blood Sample & Shipment Notification Form in Cardboard Shipper
Fill out completely during study visit
Include Kit Number Label on Form
Take a copy of each form prior to shipment. E-mail or fax NCRAD for notification
  Email: alzstudy@iu.edu
  Fax: 317-321-2003
Notes: You will need one physical form included in shipment and also send an electronic copy to us before your package goes out. If there are 8 cryboxes, we should receive 8 of these forms.

## Slide 26: Specimen Packaging and Shipment: Cardboard Package Labeling
Net weight of dry ice in kg
Dangerous Goods Label
Additional Training Required
20
Step 6.
Notes: 20 kg is 40 lbs

## Slide 27
Creating Airbills & Scheduling Pickups

## Slide 28: Shipping Accounts
https://redcap.link/BENFOaccountsurvey
One person from each site must fill out this survey in order to set up accounts with NCRAD.

## Slide 29: Navigating UPS ShipExec Tutorial
https://ncrad.org/shipping_address.html

## Slide 30: UPS ShipExecTM Thin Client Website
Log into the ShipExec Thin Client: https://kits.iu.edu/UPS
Click on the “Shipping” dropdown and click on “Shipping and Rating”

## Slide 31: Creating Airbills & Scheduling Pick Ups: Finding your Contact Information
On the right side of the screen, choose the name of your study from the “Study Group” drop down menu
  This step must be done 1st
On the left side of the screen, Click on the magnifying glass icon

## Slide 32
On the right side of the screen, a list of all the site addresses within the study you selected should populate
User can filter the search for their address further by filling in the “Company”, “Contact”, or “Address 1” fields
Please verify that both the shipping information AND study reference are correct for this shipment
If any information needs to be updated, please reach out to the NCRAD Coordinator of your study
Creating Airbills & Scheduling Pick Ups: Finding your Contact Information

## Slide 33
    Enter the total weight of your package in the “Weight” field
    Enter the dry ice weight in the “Dry Ice Weight” field
      The “Dry Ice Weight” field cannot be higher than the “Weight” field (will receive an error message)
Creating Airbills & Scheduling Pick Ups: Entering Shipment Information

## Slide 34: Creating Airbills & Scheduling Pick Ups: Scheduling Pickup Request
Click on the “Pickup Request” button
Fill out all fields for the pickup request
Enter in the “Earliest Time Ready” and “Latest Time Ready” in 24-hour format separated by colon.
Choose a name and number that is the best to contact if the UPS driver has questions related to picking up your package
Entering the Room Number and Floor will help the UPS driver locate your package
Hit “Save” when done

## Slide 35
If all fields in “Ship From” and “Shipment Information” fields are completed, and pickup request is completed (if necessary) then click “Ship” in the bottom right corner of the page
Creating Airbills & Scheduling Pick Ups: Shipping Packages

## Slide 36
Check Pickup Status by going to UPS.com, click on the Shipping, select Schedule a Pickup, and look on the right side of screen to click on “Pickup Request Status”. Enter in the Pickup No. listed on receipt into PRN field and submit
Shipment Receipt
Airbill

## Slide 37
To reprint airbill or void a shipment, click “History” at the top of the ShipExec Thin Client portal
If your shipment doesn’t automatically pop up, enter in the date of shipment and then click “Search”
Reprint
Void
Creating Airbills & Scheduling Pick Ups: Reprinting/Voiding Airbills

## Slide 38: Requirements Prior to Collections:
Material transfer agreement
Master Material Transfer Agreement must be in place with Institution prior to receiving kits from NCRAD
Appendix A for BenfoTeam study must be completed by Investigator prior to receiving kits from NCRAD
IATA biospecimen shipment training
All study personnel responsible for shipping should be certified in biospecimen shipping
It is the sites responsibility to provide additional training according to federal regulations including UN3373 Biological Substance Category B
Resources:
International Air Transport Association Training (IATA) www.iata.org
UN3373 http://hasmat.dot.gov

## Slide 39
Non-Conformance Issues

## Slide 40
Non-Conformance | Solution
Low volume aliquots | Put cryovials in a row, aliquoting in order until sample is depleted
Tubes received frozen at an angle/inverted | Carefully place tubes upright in freezer and in shipper
Aliquots are not labeled or labeled incorrectly | Refer to training or MOP for correct label placement. Save all labels until samples are packed for shipping.
All frozen samples for one participant are not sent within one shipment box | Keep plasma and buffy coat for individual participants together. Use one cryobox per participant
Fields on Blood Sample and Shipment Form left blank or incorrect data is given | Complete Blood Sample and Shipment Form during participant’s study visit while samples are processed
Blood Sample and Shipment Forms are not e-mailed or faxed to NCRAD before shipment arrives | Make copy of participants completed form after visit and save until shipment.

## Slide 41: Resources
Kit Request Module: www.kits.iu/BENFO
Screening Visit Reporter: www.kits.iu.edu/BENFOScreening
BENFO Webpage: www.ncrad.iu.edu/resource/BenfoTeam

## Slide 42: Contact Information
Questions?
Please Contact NCRAD Coordinator at:
  Phone: 1-800-526-2839
  Benfo Coordinator E-mail: eridelan@iu.edu
  NCRAD General E-mail: alzstudy@iu.edu
  Website: www.NCRAD.org